## Slide 1: ME 200 Thermodynamics
Lecture 06 – Properties

## Slide 2
Methods for Determining States
Tables
Figures
Equation of States (EOS)
Computer
Notes: We will not use computer, since the computer gets information from the tables, figures and equations of states

## Slide 3
Figures
Figures
Temperature–entropy diagram for water (SI units).

## Slide 4
Tables

## Slide 5
Tables
p
v
A-2
A-3
A-4
A-5
A-6

## Slide 6
Tables
Connection Between Property Tables and
the L-V Phase Diagram
Psat
1 x 10-3
Notes: Does not apply for an incompressible fluid. For example, given T & v => u is known, but h is not.

## Slide 7
Tables
First determine the phase (liquid, saturated or vapor)
Use the proper table, interpolation is often method needed to find the wanted values for the state
General form for properties in saturated region

## Slide 8
Interpolation
y = linear interpolation value
x = independent variable
x1,y1 = values of the function at one point
x2,y3 = values of the function at another point

## Slide 9
Extrapolation?
There are two types of people in this world:
1. Those who can extrapolate incomplete data.

## Slide 10
To Determine the Phase
Lookup T
If given p > psat
If given p < psat
Consider the case when T & p are given:

## Slide 11
To Determine the Phase
Lookup p
If given T < Tsat
If given T > Tsat
Consider the case when T & p are given:

## Slide 12
To Determine the Phase
Consider the case when either T or p plus another property are given:
Lookup T or p at saturation Table A-2 or A-3
Compare another property with it

## Slide 13
Get your textbook!
What is the value of the specific volume of a saturated liquid, vf, at 30oC?
32.894 m3/kg
1.0043 m3/kg
1.0043 × 10-3 m3/kg
1.0043 × 103 m3/kg
0.04246 m3/kg

## Slide 14
Get your textbook!
What is the saturation pressure of water at 80oC?
0.4739 bar
295.1 bar
0.06 bar
25 bar
0.35 bar

## Slide 15
Example
Water is at 5 MPa and 30 oC. Find specific volume?